PART 1 – GENERAL

1.01 SUMMARY

A. Prism™ Solid Surface Sheet

1.02 SECTION INCLUDES

A. Solid Surface sheet

1.03 REFERENCES

- American National Standards Institute (ANSI)

- International Cast Polymer Alliance (ICPA)

- National Fire Protection Association (NFPA)

- Greenguard

1.04 SYSTEM DESCRIPTION

- Provide solid surface sheet that conforms to the following requirements of regulatory agencies and the quality control of Inpro® Corporation.

- Provide solid surface material that conforms to ANSI/ICPA SS-1 for workmanship and finish, structural integrity and material characteristics.

- Fungal and Bacterial Resistance: Provide Prism™ Solid Surface that does not support fungal or bacterial growth as tested in accordance with ASTM G-21 and ASTM G-22.

- Fire Performance Characteristics: Provide Prism™ Solid Surface Sheet conforming with the NFPA class A fire rating as determined by ASTM E-84.

- Provide solid surface material that meets the emission level requirements of Greenguard certification, with results satisfying the chemical emissions requirement of California Section 1350.

- Provide solid surface material that meets the requirements of Greenguard Children and School Chemical emissions level.

1.05 SUBMITTALS

- Product Data: Manufacturer’s printed product data for each type of sheet specified.

- Samples: Color samples a minimum of 1.5" x 3" indicating color and pattern.

- Manufacturer’s Installation Instructions: Printed installation instructions for each type of sheet specified.

1.06 DELIVERY STORAGE AND HANDLING

- Deliver materials in unopened factory packaging to the jobsite.

- Inspect materials at delivery to assure that specified products have been received.

- Store in original packaging in an interior climate controlled location away from direct sunlight.

1.07 PROJECT CONDITIONS

- Environmental Requirements: Products must be installed in an interior climate controlled environment.

1.08 WARRANTY

- Standard Prism™ Solid Surface Limited 10 Year Warranty against material and manufacturing defects

PART 2 – PRODUCTS

2.01 MANUFACTURER

- Acceptable Manufacturer: Inpro® Corporation

PO Box 406 Muskego, WI 53150 USA

Telephone: 800.222.5556, Fax: 888.715.8407

inprocorp.com

- Substitutions: Not permitted

- Provide all Solid Surface Sheet from a single source.

2.02 MANUFACTURED UNITS

  - Solid Surface Sheet

    - 1/4" thickness

- Sizes, width x length

30” wide x 84”, 96”, 108”, & 120” lengths

36” wide x 84”, 96”, 108”, & 120” lengths

48” wide x 84”, 96”, 108”, & 120” lengths

60” wide x 84” & 96” lengths

Custom sizes: specify

- Edge Options:

    - Unfinished

    - Eased

    - Radius

    - Beveled

    - Wavy Edge

2.03 ACCESSORIES

  - Trim Options:

    - Inside Corner Wedge Molding, 15/16”

    - Inside Corner Molding - L-Shaped, 1” x 1”

    - Batten Strip, 2 1/2”

    - Outside Corner Molding - L-Shaped 1” x 1”

    - Perimeter Trim, 2 1/2” x 1/2”

    - Outside Corner Perimeter Trim, 2 1/2” x 1”

    - Panel Molding, 2 1/4” x 13/16”

    - Wall Base, 5” x 1/2”

    - Beveled Edge Trim, 1 3/16” x 1/2”

  - Recessed Dishes:

    - Oval Recessed Soap Dish, 9” x 8 3/4”

    - Large Shower Caddy, 7 7/8” x 15” x 3 5/8”

    - Small Shower Caddy, 8” x 6 5/8” x 2 3/4”

    - Recessed Toiletry Shelf, 12” x 18”

    - Recessed Toiletry Niche, 10” x 16”

  - Corner Shelves:

    - Small Corner Shelf, 5” x 1/2”

    - Large Corner Shelf, 8” x 1/2”

  - Corner Dishes:

    - Small Soap Dish, 4 1/8” x 4 1/8”

    - Large Soap Dish, 7 1/8” x 7 1/8”

    - Large Corner Shower Caddy, 7 1/4” x 7 1/4” x 20”

  - Solid Surface Bonding Adhesive

  - Adhesive Cartridge Dispenser

  - Adhesive Mixing Tips

  - Silicone Adhesive/Sealant

  - Pick Resistant Color Coordinated Caulk (Sealant)

2.04 MATERIALS

- Solid Surface: Prism™ Solid Surface material shall be manufactured from polyester/acrylic blended resins with natural filler material.

2.05 FINISHES

- Select color from Inpro® Corporation Prism™ Solid Surface color palette.

2.06 FABRICATION

- Fabricator should be familiar with the cutting, machining, sanding, polishing and seaming of solid surface materials.

- Produce joints connecting components using manufacturer’s joint adhesive. Joints shall be inconspicuous in appearance.

- Finish: Finish all surfaces uniformly.

PART 3 – EXECUTION

3.01 EXAMINATION

- Examine areas and conditions in which wall cladding will be installed.

3.02 PREPARATION

- General: Prior to installation, clean area to remove dust, debris and loose particles.

3.03 INSTALLATION

  - General: Install components plumb and level, scribe adjacent finishes, in accordance with approved shop drawings and recommended installation instructions.

3.04 CLEANING

  - At completion of the installation, clean surfaces in accordance with the Inpro ® Decorative Surfaces clean-up and maintenance instructions.

END OF SECTION